## Slide 3
Row Conn 1
Column Conn 1
Column Conn 2
I2C
Pwr
C_EXP_B
C_EXP_T
C_BRIDGE_B
PWR_EXP_B
PWR_EXP_T
I2C_EXP_T
I2C_EXP_B
R_EXP_B
R_EXP_T
R_SIGNAL_LX
R_BRIDGE_LX
Row Conn 2
R_EXP_B
R_EXP_T
R_BRIDGE_RX
R_SIGNAL_RX
C_EXP_B
C_EXP_T
C_SIGNAL_T
C_BRIDGE_T
C_SIGNAL_B

## Slide 7
Vdd
Sda_in
Scl_in
gnd
USB
MCP2221A
LTC4316
RL11 | RL12 | RL13 | RL14 | RL15 | RL16 | RL17 | RL18
RL21 | RL22 | RL23 | RL24 | RL25 | RL26 | RL27 | RL28
RL31 | RL32 | RL33 | RL34 | RL35 | RL36 | RL37 | RL38
RL41 | RL42 | RL43 | RL44 | RL45 | RL46 | RL47 | RL48
RL51 | RL52 | RL53 | RL54 | RL55 | RL56 | RL57 | RL58
RL61 | RL62 | RL63 | RL64 | RL65 | RL66 | RL67 | RL68
RL71 | RL72 | RL73 | RL74 | RL75 | RL76 | RL77 | RL78
RL81 | RL82 | RL83 | RL84 | RL85 | RL86 | RL87 | RL88
 | MCP23017 – 16bit IO Expander |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 0 | 0 | A2 | A1 | A0 | RW | 7 bit | 8 bit
Control rows 1 and 2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 40
Control rows 3 and 4 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 21 | 42
Control rows 5 and 6 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 22 | 44
Control rows 7 and 8 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 23 | 46
 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 24 | 48
 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 25 | 4A
 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 26 | 4C
 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 27 | 4E
A2 | A1 | A0
0 | 0 | 0
A2 | A1 | A0
0 | 0 | 1
A2 | A1 | A0
0 | 1 | 0
A2 | A1 | A0
0 | 1 | 1
7 bit TRanslation BYTE |  |  |  |  |  | 
MSB |  |  | LSB |  | fixed | 
a6 | a5 | a4 | a3 | a2 | a1 | a0
addr_out
addr_in
addr_out =XOR(ADDR_in,tr_byte)
MCP23017
MCP23017
MCP23017
MCP23017
board matrix
default
Address
2nd board matrix
Optional
address
Using the translator and 5 bits of the translation byte, it is possible to handle 25 = 32 matrix boards, each one with the default I2C addresses
Using the second matrix board with the optional addresses we can have 24x2=32 matrix boards
GPA0
:
GPA7
GPB0
:
GPB7
GPA0
:
GPA7
GPB0
:
GPB7
GPA0
:
GPA7
GPB0
:
GPB7
GPA0
:
GPA7
GPB0
:
GPB7
GPA0
GPA1
GPA2
GPA3
GPA4
GPA5
GPA6
GPA7
GPB0
GPB1
GPB2
GPB3
GPB4
GPB5
GPB6
GPB7
GPA0
GPA1
GPA2
GPA3
GPA4
GPA5
GPA6
GPA7
GPB0
GPB1
GPB2
GPB3
GPB4
GPB5
GPB6
GPB7
GPA0
GPA1
GPA2
GPA3
GPA4
GPA5
GPA6
GPA7
GPB0
GPB1
GPB2
GPB3
GPB4
GPB5
GPB6
GPB7
GPA0
GPA1
GPA2
GPA3
GPA4
GPA5
GPA6
GPA7
GPB0
GPB1
GPB2
GPB3
GPB4
GPB5
GPB6
GPB7
SCL_in
SCL_out

## Slide 9
ADDR IN |  |  |  |  |  |  |  | 7-bit Translation byte |  |  |  |  |  |  |  | ADDR OUT |  |  |  |  |  |  | 
Ext address |  |  |  |  |  |  |  | MSB |  |  | LSB |  | fixed |  | RW | Internal address |  |  |  |  |  |  | 
b7 | b6 | b5 | b4 | b3 | b2 | b1 | RW | a6 | a5 | a4 | a3 | a2 | a1 | a0 | 0 | b7 | b6 | b5 | b4 | A2 | A1 | A0 | RW
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
ADDR IN |  |  |  |  |  |  |  | 7-bit Translation byte |  |  |  |  |  |  |  | ADDR OUT |  |  |  |  |  |  | 
Ext address |  |  |  |  |  |  |  | MSB |  |  | LSB |  | fixed |  | RW | Internal address |  |  |  |  |  |  | 
b7 | b6 | b5 | b4 | b3 | b2 | b1 | RW | a6 | a5 | a4 | a3 | a2 | a1 | a0 | 0 | b7 | b6 | b5 | b4 | A2 | A1 | A0 | RW
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
Board 1
Board 2
Board 3
Board 4
Board 1
Board 2
Board 3
Board 4
The LTC4316 enables the hardwired address of one or more I2C or SMBus slave devices to be translated to a different address. This allows slaves with the same hardwired address to coexist on the same bus. Only discrete resistors are needed to select the new address and no software programming is required. Up to 127 different address translations are available.
The LTC4316 incorporates a pass-through mode which disables the address translation and allows general call addressing by the master. The LTC4316 is designed to automatically recover from abnormal bus conditions like bus stuck low or premature STOP bits.

## Slide 10
Each MCP23017 controls a pair of rows, which means 2x8=16 relays.
INPUT POLARITY REGISTER
This register allows the user to configure the polarity on
the corresponding GPIO port bits.
If a bit is set, the corresponding GPIO register bit will reflect the inverted value on the pin. Then, we MUST LEAVE the DEFAULT setting.
I/O DIRECTION REGISTER – IODIRA and IODIRB
Controls the direction of the data I/O.
When a bit is set, the corresponding pin becomes an
input. When a bit is clear, the corresponding pin
becomes an output.
Write Reg0x00=00h -> Set GPAx pin as output
Write Reg0x01=00h -> Set GPBx pin as output
PORT REGISTER – GPIOA (odd rows) GPIOB (even Rows)
The GPIO register reflects the value on the port.
GP<7:0>: Reflects the logic level on the pins <7:0>
1 = Logic-high -> CLOSE THE RELAY
0 = Logic-low -> OPEN THE RELAY

## Slide 11
 | GPA7/GPB7 | GPA6/GPB6 | GPA5/GPB5 | GPA4/GPB4 | GPA3/GPB3 | GPA2/GPB2 | GPA1/GPB1 | GPA0/GPB0 | 
 | RLx8 | RLx7 | RLx6 | RLx5 | RLx4 | RLx3 | RLx2 | RLx1 | Status
00 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | OPEN
01 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | CLOSE
02 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | CLOSE
04 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | CLOSE
08 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | CLOSE
10 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | CLOSE
20 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | CLOSE
40 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | CLOSE
80 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | CLOSE
Configure the board Matrix (7-bit address)
Write 0x20_0x00_0x00 -> Configure GPA0:7 as output
Write 0x20_0x01_0x00 -> Configure GPB0:7 as output
Write 0x21_0x00_0x00 -> Configure GPA0:7 as output
Write 0x21_0x01_0x00 -> Configure GPB0:7 as output
Write 0x22_0x00_0x00 -> Configure GPA0:7 as output
Write 0x22_0x01_0x00 -> Configure GPB0:7 as output
Write 0x23_0x00_0x00 -> Configure GPA0:7 as output
Write 0x23_0x01_0x00 -> Configure GPB0:7 as output
Example:
Control Relay row 1, column 1 -> RL11
Write 0x20_0x12_0x01 -> Close the relay
Write 0x20_0x12_0x00 -> Open the relay
Control Relay row 3, column 6 -> RL36
Write 0x21_0x12_0x10 -> Close the relay
Write 0x21_0x12_0x00 -> Open the relay
Control Relay row 8, column 8 -> RL88
Write 0x23_0x13_0x80 -> Close the relay
Write 0x23_0x13_0x00 -> Open the relay

## Slide 12
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Matrix 8x16 (8 rows and 16 columns)
HW configuration
Board 1: Short J803
Board 2: Short J803
Board 1 and Board 2: S1.A0=0, S1.A1=0, S1.A2=0
Board 1 and Board 2: S200.A0=1, S200.A1=0, S200.A2=0
Board 1 and Board 2: S400.A0=0, S400.A1=1, S400.A2=0
Board 1 and Board 2: S600.A0=0, S600.A1=1, S600.A2=1
Board 1: 7-bit Translation byte board 1 – set 0000000: S800.SW1 Closed, S800.SW5 Closed
External 7-bit address Board 1: 20h, 21h, 22h, 23h (8-bit address 40h, 42h, 44h, 46h)
Board 2: 7-bit Translation byte board 2 – set 0000100: S800.SW2 Closed, S800.SW5 Closed
External 7-bit address Board 2: 24h, 25h, 26h, 27h (8-bit address 48h, 4Ah, 4Ch, 4Eh)
SW configuration 2 boards Matrix (7-bit address)
Write 0x20_0x00_0x00 -> Configure GPA0:7 as output
Write 0x20_0x01_0x00 -> Configure GPB0:7 as output
Write 0x21_0x00_0x00 -> Configure GPA0:7 as output
Write 0x21_0x01_0x00 -> Configure GPB0:7 as output
Write 0x22_0x00_0x00 -> Configure GPA0:7 as output
Write 0x22_0x01_0x00 -> Configure GPB0:7 as output
Write 0x23_0x00_0x00 -> Configure GPA0:7 as output
Write 0x23_0x01_0x00 -> Configure GPB0:7 as output
Write 0x24_0x00_0x00 -> Configure GPA0:7 as output
Write 0x24_0x01_0x00 -> Configure GPB0:7 as output
Write 0x25_0x00_0x00 -> Configure GPA0:7 as output
Write 0x25_0x01_0x00 -> Configure GPB0:7 as output
Write 0x26_0x00_0x00 -> Configure GPA0:7 as output
Write 0x26_0x01_0x00 -> Configure GPB0:7 as output
Write 0x27_0x00_0x00 -> Configure GPA0:7 as output
Write 0x27_0x01_0x00 -> Configure GPB0:7 as output
Board 1
Board 2
Example:
Control Relay row 1, column 1 -> RL11
Write 0x20_0x12_0x01 -> Close the relay
Write 0x20_0x12_0x00 -> Open the relay
Control Relay row 6, column 13 -> RL65
Write 0x26_0x13_0x10 -> Close the relay
Write 0x26_0x13_0x00 -> Open the relay

## Slide 13
Matrix 2 independent 8x8 (2x (8 rows and 8 columns))
HW configuration
Board 1 and Board 2: S1.A0=0, S1.A1=0, S1.A2=0
Board 1 and Board 2: S200.A0=1, S200.A1=0, S200.A2=0
Board 1 and Board 2: S400.A0=0, S400.A1=1, S400.A2=0
Board 1 and Board 2: S600.A0=0, S600.A1=1, S600.A2=1
Board 1: 7-bit Translation byte board 1 – set 0000000: S800.SW1 Closed, S800.SW5 Closed
External 7-bit address Board 1: 20h, 21h, 22h, 23h (8-bit address 40h, 42h, 44h, 46h)
Board 2: 7-bit Translation byte board 2 – set 0000100: S800.SW2 Closed, S800.SW5 Closed
External 7-bit address Board 2: 24h, 25h, 26h, 27h (8-bit address 48h, 4Ah, 4Ch, 4Eh)
SW configuration 2 boards Matrix (7-bit address)
Write 0x20_0x00_0x00 -> Configure GPA0:7 as output
Write 0x20_0x01_0x00 -> Configure GPB0:7 as output
Write 0x21_0x00_0x00 -> Configure GPA0:7 as output
Write 0x21_0x01_0x00 -> Configure GPB0:7 as output
Write 0x22_0x00_0x00 -> Configure GPA0:7 as output
Write 0x22_0x01_0x00 -> Configure GPB0:7 as output
Write 0x23_0x00_0x00 -> Configure GPA0:7 as output
Write 0x23_0x01_0x00 -> Configure GPB0:7 as output
Write 0x24_0x00_0x00 -> Configure GPA0:7 as output
Write 0x24_0x01_0x00 -> Configure GPB0:7 as output
Write 0x25_0x00_0x00 -> Configure GPA0:7 as output
Write 0x25_0x01_0x00 -> Configure GPB0:7 as output
Write 0x26_0x00_0x00 -> Configure GPA0:7 as output
Write 0x26_0x01_0x00 -> Configure GPB0:7 as output
Write 0x27_0x00_0x00 -> Configure GPA0:7 as output
Write 0x27_0x01_0x00 -> Configure GPB0:7 as output
SW Relays control
Control Relay row 1, column 1 -> RL11
Write 0x20_0x12_0x01 -> Close the relay: connect SDWN to BE+ and GND_S to GND
Write 0x20_0x12_0x00 -> Open the relays
Control Relay row 1, column 2 -> RL12
Write 0x20_0x12_0x02 -> Close the relay: connect SDWN to VM+ and GND_S to GND
Write 0x20_0x12_0x00 -> Open the relays
Control Relay row 1, column 5 -> RL15
Write 0x20_0x12_0x10 -> Close the relay: connect SDWN to Supply 1.8V and GND_S to GND
Write 0x20_0x12_0x00 -> Open the relays
Control Relay row 2, column 2 -> RL22
Write 0x20_0x13_0x02 -> Close the relay: connect VBSO_S to VM+ and GND_S to GND
Write 0x20_0x13_0x00 -> Open the relays
Control Relay row 3, column 2 -> RL32
Write 0x21_0x12_0x02 -> Close the relay: connect VBAT_S to VM+ and GND_S to GND
Write 0x21_0x12_0x00 -> Open the relays
Control Relay row 4, column 2 -> RL42
Write 0x21_0x13_0x02 -> Close the relay: connect SW_S to VM+ and GND_S to GND
Write 0x21_0x13_0x00 -> Open the relays
RL11 | RL12 | RL13 | RL14 | RL15 | RL16 | RL17 | RL18
RL21 | RL22 | RL23 | RL24 | RL25 | RL26 | RL27 | RL28
RL31 | RL32 | RL33 | RL34 | RL35 | RL36 | RL37 | RL38
RL41 | RL42 | RL43 | RL44 | RL45 | RL46 | RL47 | RL48
RL51 | RL52 | RL53 | RL54 | RL55 | RL56 | RL57 | RL58
RL61 | RL62 | RL63 | RL64 | RL65 | RL66 | RL67 | RL68
RL71 | RL72 | RL73 | RL74 | RL75 | RL76 | RL77 | RL78
RL81 | RL82 | RL83 | RL84 | RL85 | RL86 | RL87 | RL88
H | L
SDWN | GND_S
VBSO_S | GND_S
VBAT_S | GND_S
SW_S | GND_S
BIAS_S | GND_S
BIAS_F | GND_S
BSO_F | GND_S
SW_F_PIN | GND_S
H | L
Battery Emulator (BE) | GND (BE-)
Voltmeter (VM) | GND (VM-)
SUPPLY 5V->12V | GND
SUPPLY 3.6V ->11V ->19V | GND
Supply 1.8V | GND
IVM6311 – conn1
H | L
Control Relay row 5, column 2 -> RL52
Write 0x22_0x12_0x02 -> Close the relay: connect BIAS_S to VM+ and GND_S to GND
Write 0x22_0x12_0x00 -> Open the relays
Control Relay row 6, column 3 -> RL63
Write 0x22_0x13_0x04 -> Close the relay: connect BIAS_F to Supply 5V-> 12V and GND_S to GND
Write 0x22_0x13_0x00 -> Open the relays
Control Relay row 6, column 4 -> RL64
Write 0x22_0x13_0x08 -> Close the relay connect BIAS_F to Supply 3.6V-> 11V->19V and GND_S to GND
Write 0x22_0x13_0x00 -> Open the relays
Control Relay row 7, column 1 -> RL71
Write 0x23_0x12_0x01 -> Close the relay: connect BSO_F to BE+ and GND_S to GND
Write 0x23_0x12_0x00 -> Open the relays
Control Relay row 7, column 3 -> RL73
Write 0x23_0x12_0x04 -> Close the relay: connect BSO_F to Supply 5V-> 12V and GND_S to GND
Write 0x23_0x12_0x00 -> Open the relays
Control Relay row 7, column 4 -> RL74
Write 0x23_0x12_0x08 -> Close the relay : connect BSO_F to Supply 3.6V-> 11V->19V and GND_S to GND
Write 0x23_0x12_0x00 -> Open the relays
Control Relay row 8, column 1 -> RL81
Write 0x23_0x13_0x01 -> Close the relay: connect SW_F_PIN to BE+ and GND_S to GND
Write 0x23_0x13_0x00 -> Open the relays
Board 1

## Slide 14
Matrix 2 independent 8x8 (2x (8 rows and 8 columns)) - Continued
SW Relays control
Control Relay row 1, column 2 -> RL12
Write 0x24_0x12_0x02 -> Close the relay: connect BCLK to BCLK AP and SDI to SDOAP
Write 0x24_0x12_0x00 -> Open the relays
Control Relay row 1, column 3 -> RL13
Write 0x24_0x12_0x04 -> Close the relay: connect BCLK to PDMCLK AP and SDI to PDM DATA AP
Write 0x24_0x12_0x00 -> Open the relays
Control Relay row 1, column 4 -> RL14
Write 0x24_0x12_0x08 -> Close the relay: connect BCLK to ANA OUT N AP and SDI to ANA OUTP AP AC
Write 0x24_0x12_0x00 -> Open the relays
Control Relay row 1, column 5 -> RL15
Write 0x24_0x12_0x10 -> Close the relay: connect BCLK to ANA OUT N AP and SDI to ANA OUT AP DC
Write 0x24_0x12_0x00 -> Open the relays
Control Relay row 2, column 1 -> RL21
Write 0x24_0x13_0x01 -> Close the relay: connect FSYN to FSYN AP and GND to GND
Write 0x24_0x13_0x00 -> Open the relays
Control Relay row 2, column 6 -> RL26
Write 0x24_0x13_0x20 -> Close the relay: connect FSYN to VDD_EXT and GND to GND
Write 0x24_0x13_0x00 -> Open the relays
Control Relay row 2, column 8 -> RL28
Write 0x24_0x13_0x80 -> Close the relay: connect FSYN to Voltmeter and GND to GND
Write 0x24_0x13_0x00 -> Open the relays
Control Relay row 3, column 6 -> RL36
Write 0x25_0x12_0x20 -> Close the relay: connect SDA to VDD_EXT and GND to GND
Write 0x25_0x12_0x00 -> Open the relays
Control Relay row 3, column 8 -> RL38
Write 0x25_0x12_0x80 -> Close the relay: connect SDA to Voltmeter and GND to GND
Write 0x25_0x12_0x00 -> Open the relays
Control Relay row 4, column 6 -> RL46
Write 0x25_0x13_0x20 -> Close the relay : connect SCL to VDD_EXT and GND to GND
Write 0x25_0x13_0x00 -> Open the relays
Control Relay row 4, column 8 -> RL48
Write 0x25_0x13_0x80 -> Close the relay: connect SCL to Voltmeter and GND to GND
Write 0x25_0x13_0x00 -> Open the relays
Control Relay row 5, column 6 -> RL56
Write 0x26_0x13_0x20 -> Close the relay: connect BCLK to VDD_EXT and GND to GND
Write 0x26_0x13_0x00 -> Open the relays
Control Relay row 5, column 8 -> RL58
Write 0x26_0x13_0x80 -> Close the relay: connect BCLK to Voltmeter and GND to GND
Write 0x26_0x13_0x00 -> Open the relays
Control Relay row 6, column 6 -> RL66
Write 0x26_0x13_0x20 -> Close the relay: connect SDI to VDD_EXT and GND to GND
Write 0x26_0x13_0x00 -> Open the relays
Control Relay row 6, column 8 -> RL68
Write 0x26_0x13_0x80 -> Close the relay: connect SDI to Voltmeter and GND to GND
Write 0x26_0x13_0x00 -> Open the relays
Control Relay row 7, column 6 -> RL76
Write 0x27_0x13_0x20 -> Close the relay: connect VDD to VDD_EXT and GND to GND
Write 0x27_0x13_0x00 -> Open the relays
Control Relay row 7, column 8 -> RL78
Write 0x27_0x13_0x80 -> Close the relay: connect VDD to Voltmeter and GND to GND
Write 0x27_0x13_0x00 -> Open the relays
RL11 | RL12 | RL13 | RL14 | RL15 | RL16 | RL17 | RL18
RL21 | RL22 | RL23 | RL24 | RL25 | RL26 | RL27 | RL28
RL31 | RL32 | RL33 | RL34 | RL35 | RL36 | RL37 | RL38
RL41 | RL42 | RL43 | RL44 | RL45 | RL46 | RL47 | RL48
RL51 | RL52 | RL53 | RL54 | RL55 | RL56 | RL57 | RL58
RL61 | RL62 | RL63 | RL64 | RL65 | RL66 | RL67 | RL68
RL71 | RL72 | RL73 | RL74 | RL75 | RL76 | RL77 | RL78
RL81 | RL82 | RL83 | RL84 | RL85 | RL86 | RL87 | RL88
H | L
BCLK | SDI
FSYN | GND
SDA | GND
SCL | GND
BCLK | GND
SDI | GND
VDD | GND
SW_F | GND
IVM6311 – conn2
IVM6311 – conn3
H | L
Board 2
H | L
FSYN AP | GND
BCLK AP | SDOAP
PDMCLK AP | PDM DATA AP
ANA OUT N AP | ANA OUTP AP AC
ANA OUT N AP | ANA OUTP AP DC
VDD_EXT | GND
VBAT_PWR_EXT | GND
Voltmeter | GND
L |  |  |  |  |  |  |  |  | 
H |  |  |  |  |  |  |  |  | 
Control Relay row 8, column 7 -> RL87
Write 0x27_0x13_0x40 -> Close the relay: connect SW_F to VBAT_PWR_EXT and GND to GND
Write 0x27_0x13_0x00 -> Open the relays